## Slide 1: PPO-Based Control of an Active Motion Surface for Parcel Singulation
Matteo G. Cigada 10767277
Marco Davi’ 10809038
Simone D’Inca’ 10837331
Final policy selection and robustness assessment
Prof. Loris Roveda - Machine Learning for Mechanical Systems - A.Y. 2025-2026

## Slide 2: Contents
Environment, reward, and physical KPI
  AMS model, downstream reward, and edge-based metric
PPO baseline
  2000-episode reference configuration and KPIs
Bayesian-optimized PPO Policy
  High-fidelity BO and best candidate selection
Robustness assessment
  Multiseed validation and non-nominal stress campaign
Conclusions and Future improvements

## Slide 3: PPO acts on the AMS; singulation is evaluated downstream
Implemented system
• 5×5 AMS matrix with 0.2 m cell side
• 25 cells × 2 commands = 50 continuous actions components
• Commands: actuator rotation and velocity magnitude
Nominal parcel flow
• 10 parcels per episode, generated in pairs
• Pair generation period: 0.75 s
• Downstream treadmill speed: 1.9 m/s
Physical regions
• PPO-controlled AMS region: 0 ≤ y ≤ 1 m
• Passive downstream region: 1 ≤ y ≤ 2 m
• Final evaluation line: y = 2 m

## Slide 4: The PPO agent observes a normalized local representation of the AMS
Grid-based observation
• 5 × 5 AMS cells
• 4 features per cell
• Observation dimension: 100
Cell feature block
[xrel, yrel, dnorm, dnorm]
where:
• xrel, yrel: normalized parcel centroid position within the cell
• dnorm: normalized parcel size
• empty cells are encoded as zeros
Normalization
• Removes dependence on absolute cell coordinates
• Keeps inputs in comparable numerical ranges
• Helps PPO process all AMS cells consistently

## Slide 5: The training reward[*] promotes downstream pairwise separation
Rewarding logic
1 ≤ y ≤ 2 m
At each step:
1. Select parcels in the downstream region
2. Sort them by longitudinal position
3. Compute edge gaps between consecutive parcels
4. Convert each gap into a local score
5. Use the worst pair as instantaneous reward
Bonus:
+20 if all gaps are positive and at least three parcels are present.
Mathematical expression
Parcel 1
Parcel 2
Parcel 3
gap g1
gap g2
localScore1
y = 2 m
y = 1 m
localScore2
K = number of downstream parcels, gk = k-th edge gap
y
[*]: Roveda, Maccarini, Pura, Reiso & Spahiu (2025) Optimizing Parcels Sorting Through Reinforcement Learning for Intralogistics.

## Slide 6: Final physical performance is evaluated using parcel-edge gaps
Evaluation line
• Final parcel configuration at y = 2 m
• After the downstream region
Edge-based pair gap
• g = bottom(front parcel) − top(rear parcel)
• Centroid distance is not used
Success criterion
• Successful pair: g > 5 mm
• Reported metric: percentage of successful consecutive pairs
The reward guides learning;
final edge gaps evaluate physical singulation.

## Slide 7: The 2000-episode PPO baseline was effective but still improvable
Reference PPO setup
Experience horizon: 500
Clip factor: 0.20
Actor/Critic LR: 1e-4
GAE factor: 0.95
Discount factor: 0.99
Entropy weight: 0.01
Training seed: 1
Example nominal test rollout for the reference PPO baseline
Reference PPO physical performance
Mean final accuracy>5mm: 93.44 %
Std. Deviation: 8.66 pp
Worst episode accuracy: 66.67 %
Mean Throughput: 8250.1 pph
Mean max overlap: 0.0500m
Mean Collision count: 20.53
Evaluation seed base: 3000
Margin to improve

Margin to improve

High average performance was achieved, but worst-case episodes and residual overlap motivated PPO tuning.

## Slide 8: Bayesian Optimization candidates outperformed the reference baseline
BO setup
• 2000 training episodes per configuration
• 100 nominal evaluation episodes
• Objective:
Āgt5mm = Mean Final Accuracy>5mm
Key interpretation
• BO candidates improve both accuracy and worst-case behavior.
• BO_014 gives the best accuracy, lowest std, and lowest overlap.
• BO_018 remains a strong throughput-efficient alternative.
Final choice
BO_014 prioritizes physical singulation quality over maximum throughput.
Chart: 
| Baseline | BO_008 | BO_014 | BO_018
Mean Final Accuracy>5mm | 93.44 | 97.33 | 99.78 | 98.89
Std. Deviation | 8.66 | 4.77 | 1.56 | 3.35
Worst Episode Accuracy | 66.67 | 88.89 | 88.89 | 88.89
Set | Mean overlap [m] | Throughput [pph] | Collisions
Baseline | 0,0500 | 8250,1 | 20,53
BO_008 | 0,0222 | 8052,1 | 5,05
BO_014 | 0,00133 | 7874,2 | 1,00
BO_018 | 0,00352 | 8244,7 | 0,25
PPO parameter Baseline BO_014
Experience horizon: 500 400
Clip factor: 0.20 0.098
Actor LR: 1e-4 5,66e-5
Critic LR: 1e-4 2,96e-4
GAE factor: 0.95 0.959
Discount factor: 0.99 0.995
Entropy weight: 0.01 1,60e-4
Epochs: 3 4
Parameter shift interpretation
• Smaller clip factor and lower actor LR suggest more conservative policy updates.
• Higher critic LR and one extra epoch improve value-function fitting during PPO updates.
• Much lower entropy weight reduces exploration once the policy has learned a stable singulation behavior.
• Slightly higher discount factor keeps downstream separation more relevant in the optimization.

## Slide 9: Multiseed validation confirmed the robustness of BO_014
Chart: 
| 1 | 270632 | 278468 | 287102
Mean Final Accuracy | 99.67 | 99.78 | 96.67 | 95.33
Std. Deviation | 1.9 | 1.56 | 6.01 | 6.55
Worst Episode Accuracy | 88.89 | 88.89 | 77.78 | 77.78
Multiseed validation
• Final configuration: BO_014
• 4 independent PPO training seeds
• 100 nominal evaluation episodes per seed
Training diagnostic
• Reward trends indicate stable PPO training across seeds.
• AverageReward is not used as the final success metric.
Physical robustness
• Mean accuracy across seeds: 97.86%
• Std across training seeds: 2.22 pp
• Worst episode across all seeds: 77.78%
BO_014 is not dependent on a single PPO training realization and remains physically effective across different random seeds.
BO_014 multiseed training average reward trend

## Slide 10: Non-nominal stress tests evaluated the operating limits of BO_014
• Final configuration: BO_014
• 4 trained agents from the multiseed analysis
• 4 agents × 100 episodes per scenario
Treadmill
velocity
Generation frequency
Parcel
shape
Total parcels per episode
Parcels per generation
The goal is to distinguish robust generalization from actual operating limitations.
• Evaluation seed base: 2044876
• No retraining
• No reward, no PPO changes
Evaluation-only stress campaign

## Slide 11: Reduced treadmill velocity caused moderate degradation
Treadmill velocity = 1,30 m/s
Nominal case
Mean Final Accuracy>5mm: 98,28%
Worst Agent Accuracy: 96,33%
Mean Max Overlap: 9,9 mm
Throughput: 8027 pph
Treadmill-1p60
Mean Final Accuracy>5mm: 96,86% -1,42 pp
Worst Agent Accuracy: 93,67% -2,66 pp
Mean Max Overlap: 14,1 mm +4,2 mm
Throughput: 7874 pph -153 pph
Treadmill-1p30
Mean Final Accuracy>5mm: 94,36% -3,92 pp
Worst Agent Accuracy: 88,00% -8,33 pp
Mean Max Overlap: 24,1 mm +14,2 mm
Throughput: 7662 pph -365 pph
Treadmill velocity = 1,60 m/s
Reduced downstream speed degrades separation quality, but it is not the most critical operating limitation.

## Slide 12: Higher generation frequency revealed a temporal inflow limit
Generation frequency = 0,50 s
Nominal case
Mean Final Accuracy>5mm: 98,28%
Worst Agent Accuracy: 96,33%
Mean Max Overlap: 9,9 mm
Throughput: 8027 pph
Generation-0p60
Mean Final Accuracy>5mm: 92,36% -5,92 pp
Worst Agent Accuracy: 90,89% -5,44 pp
Mean Max Overlap: 57,9 mm +48,0 mm
Throughput: 9243 pph +1216 pph
Generation-0p50
Mean Final Accuracy>5mm: 85,22% -13,06 pp
Worst Agent Accuracy: 77,67% -18,66 pp
Mean Max Overlap: 112,9 mm +103,0 mm
Throughput: 10360 pph +2333 pph
Generation frequency = 0,60 s
The policy degrades when parcels enter the AMS too frequently, leaving less time to recover longitudinal separation.

## Slide 13: BO_014 generalized well to rectangular parcel shapes
Nominal case
Mean Final Accuracy>5mm: 98,28%
Worst Agent Accuracy: 96,33%
Mean Max Overlap: 9,9 mm
Throughput: 8027 pph
Rectangular parcels
Mean Final Accuracy>5mm: 97,42% -0,86 pp
Worst Agent Accuracy: 95,00% -1,33 pp
Mean Max Overlap: 17,9 mm +8,0 mm
Throughput: 8036 pph +9,0 pph
Rectangular dimensions randomly sampled within the nominal parcel-size bounds: [0.05, 0.40] m
The policy is not strongly tied to the nominal square-parcel assumption.

## Slide 14: Increasing the total number of parcels did not collapse performance
Nominal case
Mean Final Accuracy>5mm: 98,28%
Worst Agent Accuracy: 96,33%
Mean Max Overlap: 9,9 mm
Throughput: 8027 pph
Parcels_20
Mean Final Accuracy>5mm: 97,84% -0,44 pp
Worst Agent Accuracy: 95,84% -0,49 pp
Mean Max Overlap: 25,1 mm +15,2 mm
Throughput: 8738 pph +711 pph
The policy scales well with the total number of parcels when the nominal pairwise generation structure is preserved.

## Slide 15: Three-parcel generation was the most severe stress condition
Nominal case
Mean Final Accuracy>5mm: 98,28%
Worst Agent Accuracy: 96,33%
Mean Max Overlap: 9,9 mm
Throughput: 8027 pph
Batch3_12
Mean Final Accuracy>5mm: 78,34% -19,94 pp
Worst Agent Accuracy: 72,00% -24,33 pp
Mean Max Overlap: 112,8 mm +102,9 mm
Throughput: 11481 pph +3454 pph
At each generation event, 3 parcels enter the system in a left-center-right configuration. To avoid artificial initial overlaps and preserve AMS-grid compatibility, the upper parcel-size bound was reduced to 0.30 m.
The number of parcels per episode was set to 12, corresponding to 4 complete batches.
The main difficulty is not only temporal inflow rate, but also simultaneous spatial crowding at generation.

## Slide 16: Final outcome: strong nominal policy, clear robustness target
• Environment, reward, and physical KPIs were verified before final training.
• AverageReward was used only as a training diagnostic.
Validated formulation
• BO improved PPO over the reference baseline.
• BO_014 achieved strong nominal and multiseed performance.
Selected policy
• Shape and parcel-count variations were handled well.
• Dense and simultaneous inflow remained the main robustness limit.
Observed limitation
Next steps
Mixed high-density training · Crowding-aware observation · Congestion-aware reward terms · Curriculum learning
Future work should target robustness to dense inflow, where the current policy shows its clearest operating limit.